/*
* Star network of sensors
* Node 0 is the base and receives the data from the other units
*/

#include <SPI.h>
#include "RF24.h"
#include <printf.h>

#include <OneWire.h>
#include <DallasTemperature.h>

// Define sensor types - resist the temptation to do it right
// and use an enum because brain dead C will change the size
// of an enum across architectures (and sometimes even in the
// same architecture)
const byte NONE = 0;
const byte DS18B20 = 1;
const byte TMP36 = 2;

char *sensorTypeC[] = {"none","DS18B20","TMP36"};

// Data wire is plugged into pin 4 on the Arduino
// use data pins to supply power to the DS18B20
const byte ONE_WIRE_GND = 2;
const byte ONE_WIRE_VCC = 3;
const byte ONE_WIRE_BUS = 4;

// Setup a oneWire instance to communicate with any OneWire devices (not just Maxim/Dallas temperature ICs)
OneWire oneWire(ONE_WIRE_BUS);

// Pass our oneWire reference to Dallas Temperature.
DallasTemperature sensors(&oneWire);

// array to hold device addresses add more for multiple sensors
DeviceAddress temperatureSensor;

/****************** User Config ***************************/
/*** Bits to set this radio number ***/
const byte CONFIG0 = 6; // radio number zero bit
const byte CONFIG1 = 7; // radio number 1 bit bit
byte radioNumber;
// interface pins
const byte RF_CE = 9; // chip enable
const byte RF_CSN = 10; // SPI negative chip select
/* Hardware configuration: Set up nRF24L01 radio on SPI bus plus ce and csn */
RF24 radio(RF_CE,RF_CSN);
/**********************************************************/

byte addresses[][6] = {"0Node",
        "1Node",
        "2Node",
        "3Node",
        "4Node",
        "5Node"};

typedef struct datapacket
{ // offset
  float value; // 0 sensor value - put first for processors that have bdy requirements
  uint16_t type; // 4 sensor type
  uint16_t node; // 6 number of sensor node
} DataPacket; // total size 8

DataPacket data;

void setup() {
  // power One Wire device from I/O pins
  pinMode(ONE_WIRE_GND,OUTPUT);
  digitalWrite(ONE_WIRE_GND,LOW);
  pinMode(ONE_WIRE_VCC,OUTPUT);
  digitalWrite(ONE_WIRE_VCC,HIGH);

  Serial.begin(57600);
  printf_begin();

  // read configuration pins to see which device this is
  pinMode(CONFIG0,INPUT_PULLUP);
  pinMode(CONFIG1,INPUT_PULLUP);
  radioNumber = (digitalRead(CONFIG1)<<1) | digitalRead(CONFIG0);

  radio.begin();

  // Set the PA Level low for testing when there is
  // the likelihood of close proximity of the devices. RF24_PA_MAX is default.
// radio.setPALevel(RF24_PA_LOW);

  // set data transfer size
// radio.setPayloadSize(sizeof(data));

  if (radioNumber == 0) {
    // this is the base node that gets info from other nodes
    // Listen on all addresses
    radio.openReadingPipe(1,addresses[1]);
    radio.openReadingPipe(2,addresses[2]);
    radio.openReadingPipe(3,addresses[3]);
    radio.openReadingPipe(4,addresses[4]);
    radio.openReadingPipe(5,addresses[5]);
  }
  else {
    // Sensor node - open address for this node
    radio.openWritingPipe(addresses[radioNumber]);
    // Start up the temperature sensor library
    sensors.begin();
    oneWire.reset_search();
    if (!oneWire.search(temperatureSensor)) {
      Serial.println("Unable to find address for temperature sensor ");
      data.type = NONE;
    } else {
      data.type = DS18B20;
    }
    data.node = radioNumber;
  }
   //
  // Dump the configuration of the rf unit for debugging
  //

  radio.printDetails();

}

void loop() {
  uint8_t pipe;
  if (radioNumber == 0) {
    // this is the base node that gets info from other nodes
    // Listen on all addresses
    // Start the radio listening for data
    radio.startListening();

       while (! radio.available(&pipe)); // Wait until there is data ready
 // printf("pipe %d \n",pipe);
        radio.read( &data, sizeof(data) ); // Get the data
        printf("Node %d Sensor type %s Value ",data.node,sensorTypeC[data.type]);
        Serial.println(data.value);

  }
  else {
    // Sensor node - note print statements are mostly for
    // debugging - in actual use it won't be connected to a serial port
    // read sensor and send data
    sensors.requestTemperaturesByAddress(temperatureSensor); // Send the command to start conversion
   // After we got the temperature, we can retrieve the value
    data.value = sensors.getTempC(temperatureSensor);
    Serial.print("Node ");
    Serial.print(radioNumber);
    Serial.print(" Temperature for the sensor is: ");
    Serial.println(data.value);

    radio.stopListening(); // should not be in listen mode but just in case...
    if (!radio.write( &data, sizeof(data) )){
       Serial.println(F("failed")); // just in case we have a terminal
  // radio.printDetails();
    }
    delay(3000);
  }

} // Loop